| Section 1 Identification of the substance/mixture and of the company/undertaking |
| --- |
| 1.1 Product identifier: |
| Mixture identification Trade name: | ALUMINIUM PASTE WITH MINERAL SPIRIT AND NAPHTHA SOLVENT Aluminium Paste MG 1250 Aluminium Paste MG 1250MO Aluminium Paste MG 1200 Aluminium Paste MG 1100 Aluminium Paste 8188 NAR Aluminium Paste CA-290N Aluminium Paste CE-201N Aluminium Paste CEV120N Aluminium Paste CF-150N Aluminium Paste TZ-562JC Aluminium Paste CF-240N Aluminium Paste TZ-350A Aluminium Paste CBD110N Aluminium Paste TZ-816A Aluminium Paste TZ-788A Aluminium Paste CEF113N |
| Additional identification: | Nanoform is NOT covered by this SDS. |
| UFI: | AVNJ-U0ED-GTK7-UGE6 |
| Identification of the product: | See section 3 |
| Index Number: | See section 3 |
| REACH registration No.: | See section 3 |
| 1.2 Relevant identified uses of the substance or mixture and uses advised against: |
|  | 1.2.1 Identified uses: |
|  | Metallic paint (for automotive industry and industrial use). Manufacture of inks. Manufacture of plastics. |
|  | 1.2.2 Uses advised against: |
|  | Not available. |
| 1.3 Details of the supplier of the safety data sheet: |
| Supplier(Only representative): | - |
| Supplier(Manufacturer): | TOYAL ZHAOQING CO.,LTD |
| Address: | Lingjiang Industrial Park,Zhaoqing National High-Tech Industrial Development Zone,Guangdong, China |
| Contact person(E-mail): | yinzd@toyalchina.com wangjin@toyalchina.com |
| Telephone: | +86 (0)758 3602080 |
| Fax: | +86 (0)758 3602081 |
| 1.4 Emergency telephone Number: |
|  | +33 (0)5 59 983 556 (Toyal Europe S.A.S.U. Accous FR) Only available during office hours (9:00a.m.-17:30p.m.) |
|  | Available outside office hours? | YES |  |  | NO | X |  |
| Section 2 Hazards identification |
| 2.1 Classification of the substance or mixture: |
|  | 2.1.1 Classification of the mixture: |
| The mixture is classified as following according to REGULATION (EC) No 1272/2008: |
| REGULATION (EC) No 1272/2008 Hazard classes/Hazard categories Hazard statement STOT SE 1 H228 STOT SE 3 H336 Aquatic Chronic 3 H412 For full text of H- phrases: see section 2.2. |
| 2.2 Label elements: |
| Hazard pictogram(s): |  |
| Signal word: | DANGER |
| Hazard statement(s): | H228: Flammable solid. H336: May cause drowsiness or dizziness. H412: Harmful to aquatic life with long lasting effects. |
| Precautionary statement(s): | P210: Keep away from heat, hot surface, sparks, open flames and other ignition sources. No smoking. P240: Ground/bond container and receiving equipment. P241: Use explosion-proof [electrical/ventilating/lighting/.../] equipment. P280: Wear protective gloves/protective clothing/eye protection/face protection/hearing protection/... P261: Avoid breathing dust/fume/gas/mist/vapours/spray. P271: Use only outdoors or in a well-ventilated area. P273: Avoid release to the environment. P304 + P340: IF INHALED: Remove person to fresh air and keep comfortable for breathing. P312: Call a POISON CENTER/doctor/… if you feel unwell. P403 + P233: Store in a well-ventilated place. keep container tightly closed. P501: Dispose of contents/container in accordance with local regulations. |
| Supplemental Hazard information (EU) | Not applicable. |
| 2.3 Other hazards: |
| The mixture does not contain PBT/vPvB substance. The mixture does not contain endocrine disruptor. |
| Section 3 Composition/information on ingredients |
| Substance/Mixture: | Mixture |
| Ingredient(s): |
| Chemical Name Registration No. CAS No. EC No. Concentration Classification Specific Concentration limits, M-Factors, Acute Toxicity Estimates (ATE) Aluminium powder (stabilised) 01-2119529243-45-XXXX 7429-90-5 231-072-3 60-80% H228 H261 N/A Naphtha (petroleum), hydrotreated heavy Hydrocarbons, C9-C11, n-alkanes, isoalkanes, cyclics, <2% aromatics 01-2119463258-33-XXXX 64742-48-9 265-150-3 10-30% H226 H304 H336 N/A Aromatic Solvent (petroleum), light arom. Hydrocarbons, C9, aromatics 01-2119455851-35-XXXX 64742-95-6 265-199-0 5-13% H304 H226 H335 H336 H411 N/A Oleic acid N/A 112-80-1 204-007-1 ≤2% Not Classified N/A |
| Section 4 First aid measures |
| 4.1 Description of first aid measures: |
|  | In all cases of doubt, or when symptoms persist, seek medical attention. |
|  | 4.1.1 In case of inhalation: |
|  | Remove casualty to fresh air and keep warm and at rest. |
|  | 4.1.2 In case of skin contact: |
|  | Wash with plenty of water and soap. |
|  | 4.1.3 In case of eyes contact: |
|  | In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. |
|  | 4.1.4 In case of ingestion: |
|  | Do not under any circumstances induce vomiting. OBTAIN A MEDICAL EXAMINATION IMMEDIATELY. |
| 4.2 Most important symptoms and effects, both acute and delayed: |
|  | Harmful if inhaled. Causes skin irritation. Causes serious eye irritation. May cause respiratory irritation. May cause drowsiness or dizziness. May cause damage to organs. |
| 4.3 Indication of any immediate medical attention and special treatment needed: |
|  | If skin irritation or rash occurs, get medical advice/attention. |
| Section 5 Firefighting measures |
| 5.1 Extinguishing media: |
| Suitable extinguishing media: | Powder extinguisher, carbon dioxide gas, dry sand. |
| Unsuitable extinguishing media: | Water, extinguishing media containing water, halogen extinguishing media. |
| 5.2 Special hazards arising from the substance or mixture | In case of contact with acid or alkaline (as well as water), aluminum powder will react and emission of hydrogen will occur. |
| 5.3 Advice for firefighters: | In the event of fire, wear self-contained breathing apparatus. Use personal protective equipment. Wear chemical resistant oversuit. Cool containers / tanks with water spray. |
| Section 6 Accidental release measures |
| 6.1 Personal precautions, protective equipment and emergency procedures: |
| 6.1.1 For non-emergency personnel: | Wear personal protection equipment. Remove persons to safety. |
| 6.1.2 For emergency responders: | Evacuate personnel to safe areas. Keep people away from and upwind of spill/leak. Ventilate the area. Wear suitable protective clothing. |
| 6.2 Environmental precautions: | Should not be released into the environment. Do not flush into surface water or sanitary sewer system. If the product contaminates rivers and lakes or drains inform respective authorities. |
| 6.3 Methods and material for containment and cleaning up: | Pick up mechanically. |
| 6.4 Reference to other sections: | See Section 8 for information on personal protection equipment. See Section 13 for information on disposal. |
| Section 7 Handling and storage |
| 7.1 Precautions for safe handling: |
| 7.1.1 Protective measures: | Avoid contact with skin and eyes, inhaltion of vapours and mists. Don't use empty container before they have been cleaned. Before making transfer operations, assure that there aren't any incompatible material residuals in the containers. Contamined clothing should be changed before entering eating areas. Do not eat or drink while working. |
| 7.1.2 Advice on general occupational hygiene: | Do not eat, drink and smoke in work areas. Wash hands after use. Remove contaminated clothing and protective equipment before entering eating areas. |
| 7.2 Conditions for safe storage, including any incompatibilities: | Keep container tightly closed and store in well-ventilated areas. Store in a dry and cool place. Keep container dry. Protect from water. Do not store with: Oxidizing agents; Acids; Alkalies; Nitrates; Alcohols; Halogenated hydrocarbons; Halogens. Keep away from food, drink and feed. |
| 7.3 Specific end use(s): | Not applicable. |
| Section 8 Exposure controls/personal protection |
| 8.1 Control parameters: |
| 8.1.1 Occupational exposure limits: |  |
| Occupational Exposure Limit Value (8-hour reference period) Occupational Exposure Limit Value (15-minute reference period) Country Substance EC No. CAS No. ppm mg/m3 ppm mg/m3 Note Ireland Aluminium alkyl compounds 231-072-3 7429-90-5 - 2 - - - Germany (DFG) Naphtha (petroleum), hydrotreated heavy 265-150-3 64742-48-9 50 300 100 600 - |
| 8.1.2 Additional exposure limits under the conditions of use: | Not available. |
| 8.1.3 DNEL/DMEL and PNEC-Values: | Not available. |
| 8.2 Exposure controls: |
| 8.2.1Appropriate engineering controls: | Ensure adequate ventilation. Apply technical measures to comply with the occupational exposure limits. |
| 8.2.2 Individual protection measures, such as personal protective equipment: |
| Eye/face protection: | Eye glasses with side protection. |
| Skin protection |  |
| Hand protection: | Suitable gloves type: EN 420 / EN 374 Suitable material: Cotton. Leather |
| Body protection: | Chemical resistant apron. |
| Respiratory protection: | Use adequate protective respiratory equipment, e.g. CEN/FFP-2 or CEN/FFP-3. |
| Thermal hazards: | Wear suitable protective clothing to prevent heat. |
| 8.2.3 Environmental exposure controls: | Avoid discharge into the environment. According to local regulations, Federal and official regulations. |
| Section 9 Physical and chemical properties |
| 9.1 Information on basic physical and chemical properties: |
| Physical state: | Pasty |
| Colour: | Silver |
| Odour: | Petroleum |
| Odour threshold: | Not available |
| pH: | Not available |
| Melting point/freezing point (°C): | Not available |
| Boiling point or initial boiling point and boiling range (°C): | Not available |
| Flash point (°C): | >40°C |
| Evaporation rate: | Not available |
| Flammability limit - lower (%): | Not available |
| Flammability (gas, liquid, solid): | Not available |
| Ignition temperature (°C): | Not available |
| Lower and upper explosion limit: | Not available |
| Vapour pressure (20°C): | Not available |
| Relative vapour density: | Not available |
| Relative Density (g/cm3): | 1.4-1.8 g/cm3 (calculated) |
| Bulk density (kg/m3): | Not available |
| Solubility in water (g/l, 20°C): | Insoluble |
| Solubility in other polar and non-polar solvents (g/l, 20°C): | Not available |
| Partition coefficient n-octanol/water (log Po/w, 20°C): | Not available |
| Auto-ignition temperature: | > 200°C |
| Decomposition temperature: | Not available |
| Kinematic viscosity (mm²/s): | Not available |
| Particle characteristics: | Not available |
| Explosive properties: | Not available |
| Oxidising properties: | Not available |
| 9.2. Other information: |
| Fat solubility(solvent-oil to be specified) etc: | Not available |
| Surface tension: | Not available |
| Dissociation constant in water( pKa): | Not available |
| Oxidation-reduction Potential: | Not available |
| Section 10 Stability and Reactivity |
| 10.1 Reactivity: | The substance is stable under normal storage and handling conditions. |
| 10.2 Chemical stability: | Stable at room temperature in closed containers under normal storage and handling conditions. |
| 10.3 Possibility of hazardous reactions: | It may generate flammable gases, on contact with mineral acids. It may catch fire on contact with mineral acids, azo, diazo and hydrazine compounds, halogenated organic substances, and powerful oxidising agents. In case of contact with acid or alkaline (as well as water), aluminum powder will react and emission of hydrogen will occur. |
| 10.4 Conditions to avoid: | Incompatible materials. Exothermal reactions are possible in the event of contact with incompatible substances |
| 10.5 Incompatible materials: | Oxidizing agents; Acids; Alkalies; Nitrates; Alcohols; Halogenated hydrocarbons; Halogens. |
| 10.6 Hazardous decomposition products: | Hydrogen. |
| Section 11 Toxicological information |
| 11.1 Information on hazard classes as defined in Regulation (EC) No 1272/2008: |
| Acute toxicity: |
| ATEmix(oral): | Not available |
| ATEmix(inhalation): | Not available |
| ATEmix(Dermal): | Not available |
| Aluminium powder (stabilised) (CAS: 7429-90-5) |
| LD50(Oral, Rat): | > 15900 mg/kg bw |
| LC50(Inhalation, Rat): | > 0.888 mg/L air (analytical), male, 4h |
| LD50(Dermal, Rabbit): | Not available |
| Naphtha (petroleum), hydrotreated heavy Hydrocarbons, C9-C11, n-alkanes, isoalkanes, cyclics, <2% aromatics (CAS: 64742-48-9) |
| LD50(Oral, Rat): | > 5000 mg/kg bw |
| LC50(Inhalation, Rat): | > 9300 mg/m³ air 4h |
| LD50(Dermal, Rat): | > 2000 mg/kg bw |
| Aromatic Solvent (petroleum), light arom. Hydrocarbons, C9, aromatics (CAS: 64742-95-6) |
| LD50(Oral, Rat): | > 5000 mg/kg bw |
| LC50(Inhalation, Rat): | > 5610 mg/m³ air (analytical), 4h |
| LD50(Dermal, Rabbit): | > 2000 mg/kg bw |
| Skin corrosion/irritation: | Not classified |
| Serious eye damage/irritation: | Not classified |
| Respiratory or skin sensitization: | Not classified |
| Germ cell mutagenicity: | Not classified |
| Carcinogenicity: | Not classified |
| Reproductive toxicity: | Not classified |
| STOT- single exposure: | May cause respiratory irritation. May cause drowsiness or dizziness. |
| STOT-repeated exposure: | Not classified |
| Aspiration hazard: | Not classified |
| 11.2 Information on other hazards |
| Endocrine disrupting properties | The mixture does not contain endocrine disruptor. |
| Other information | Not applicable |
| Section 12 Ecological information |
| 12.1 Toxicity: |
| Aluminium powder (stabilised) (CAS: 7429-90-5) |
| Acute (short-term) toxicity: |  |
| LC50(96h, Fish): | 6.17 mg/L |
| EC50(48h, Crustacea): | Not available |
| EC50(72h, Algae/aquatic plants): | Not available |
| Chronic (long-term) toxicity: |  |
| NOEC(Fish): | Not available |
| NOEC(Crustacea): | Not available |
| EC50(Algae/aquatic plants): | Not available |
| Naphtha (petroleum), hydrotreated heavy Hydrocarbons, C9-C11, n-alkanes, isoalkanes, cyclics, <2% aromatics (CAS: 64742-48-9) |
| Acute (short-term) toxicity: |  |
| LC50(96h, Fish): | > 1000 mg/L |
| EC50(48h, Crustacea): | > 1000 mg/L |
| EC50(72h, Algae/aquatic plants): | > 1000 mg/L |
| Chronic (long-term) toxicity: |  |
| NOEC(Fish): | 0.131 mg/L |
| NOEC(Crustacea): | 0.23 mg/L |
| NOEC(Algae/aquatic plants): | 3 mg/L |
| Aromatic Solvent (petroleum), light arom. Hydrocarbons, C9, aromatics (CAS: 64742-95-6) |
| Acute (short-term) toxicity: |  |
| LC50(96h, Fish): | 8.2 mg/L |
| EC50(48h, Crustacea): | 4.5 mg/L |
| EC50(72h, Algae/aquatic plants): | 3.1 mg/L |
| Chronic (long-term) toxicity: |  |
| NOEC(Fish): | 2.6 mg/L |
| NOEC(Crustacea): | 2.6 mg/L |
| NOEC(Algae/aquatic plants): | 0.5 mg/L |
| 12.2 Persistence and degradability: | Not available. |
| 12.3 Bioaccumulative potential: | Not available. |
| 12.4 Mobility in soil: | Not available. |
| 12.5 Results of PBT and vPvB assessment: | The mixture does not contain PBT / vPvB substance. |
| 12.6 Endocrine disrupting properties: | The mixture does not contain endocrine disruptor. |
| 12.7 Other adverse effects: | Not available. |
| 12.8 Additional information | Not available. |
| Section 13 Disposal considerations |
| 13.1 Waste treatment methods: | Dispose of in accordance with all applicable local and national regulations. Use recovery/recycling where feasible, otherwise incineration is the recommended method of disposal. Empty containers may contain hazardous residues. Do not cut, puncture or weld on or near to the container. Labels should not be removed from containers until they have been cleaned. Contaminated containers must not be treated as household waste. Containers should be cleaned by appropriate methods and then re-used or disposed of by landfill or incineration as appropriate. Do not incinerate closed containers. |
| Section 14 Transport Information |
|  | Land transport (ADR/RID) | Inland waterways (ADN) | Sea transport (IMDG) | Air transport (ICAO/IATA) |
| 14. 1 UN number or ID number | 1325 | 1325 | 1325 | 1325 |
| 14.2 UN proper shipping name | Flammable solid organic NOS | Flammable solid organic NOS | Flammable solid organic NOS | Flammable solid organic NOS |
| 14.3 Transport hazard class(es) | 4.1 | 4.1 | 4.1 | 4.1 |
| 14.4 Packing group | ǁ | ǁ | ǁ | ǁ |
| 14.5 Environmental hazards | No | No | No | No |
| 14.6 Special precautions for user | See section 2.2 | See section 2.2 | See section 2.2 | See section 2.2 |
| 14.7 Maritime transport in bulk according to IMO instruments | IBCO8 | IBCO8 | IBCO8 | IBCO8 |
| Section 15 Regulatory information |
| 15.1 Safety, health and environmental regulations/legislation specific for the substance or mixture: |
| Relevant information regarding authorization: | Not applicable. |
| Relevant information regarding restriction: | Not applicable. |
| Other EU regulations: | Employment restrictions concerning young person must be observed. For use only by technically qualified individuals. |
| Other National regulations: | Not applicable |
| 15.2 Chemical Safety Assessment | YES |  | NO | X |  |
| Section 16 Other information |
| 16.1 Indication of changes: |
| Version 1.0 Amended by (EU) 2020/878 |
| 16.2 Abbreviations and acronyms: |
| ADR: European Agreement concerning the International Carriage of Dangerous Goods by Road RID: Regulations concerning the International Carriage of Dangerous Goods by Rail ADN: European Agreement concerning the International Carriage of Dangerous Goods by Inland Waterways IMDG: Code international maritime dangerous goods code ICAO: International Civil Aviation Organization IATA: International Air Transport Association UFI: Unique Formula Identifier LC50: median lethal concentration EC50: The effective concentration of substance that causes 50% of the maximum response. NOEC: No Observed Effect Concentration DNEL: derived no-effect level PNEC: predicted no-effect concentration |
| 16.3 Key literature references and sources for data |
| ECHA Registered substances data |
| 16.4 Classification and procedure used to derive the classification for mixtures according to Regulation (EC) 1272/2008 [CLP] |
| Classification according to Regulation (EC) No. 1272/2008 Classification procedure STOT SE 3 H336 Calculation method Aquatic Chronic 3 H412 Calculation method |
| 16.5 Relevant H-statements (number and full text): |
| H335: May cause respiratory irritation. H336: May cause drowsiness or dizziness. H412: Harmful to aquatic life with long lasting effects. |
| 16.6 Training instructions: |
| Not applicable. |
| 16.7 Further information: |
| This information is based upon the present state of our knowledge. This SDS has been compiled and is solely intended for this product. |
| 16.8 Notice to reader: |
| Employers should use this information only as a supplement to other information gathered by them, and should make independent judgment of suitability of this information to ensure proper use and protect the health and safety of employees. This information is furnished without warranty, and any use of the product not in conformance with this Safety Data Sheet, or in combination with any other product or process, is the responsibility of the user. |
| Author: Hangzhou REACH Technology Group Co., Ltd. Website:www.cirs-group.com Tel:0571-87206555 Email:info@cirs-group.com |